## Slide 1: EE-577B Project - Phase 2 Gold Variable-Width Processor
Andrew Adam
Harsh Bhardwaj

## Slide 2: Agenda
Overview of design
  Division of work
Processor Pipeline
  Register File
  Stalling
  Forwarding
  Branches
ALU
  Shifters
  Multipliers
Testing & Synthesis
Q & A

## Slide 3: Overview
Four-stage variable-width processor
Flow
  Design → RTL → Testing → Synthesis
Division of work
  Andrew
    Logical & Shift instructions
    Memory instructions
    Register File
    Program Counter
  Harsh
    Arithmetic instructions
    Branch instructions
    Perl compiler script
  Both
    Pipeline structure and components
    ALU
3

## Slide 4: High-level Block Diagram
Data
Control

## Slide 5: Processor Pipeline - Register File
Tradeoff between 1-D [width*depth] vs 2-D reg file [width][depth]
Key Features:
  Internally forward if write address = read address
  Participation fields used in reg file
    1) Ex stage calculation assumes all fields participate
    2) Reg file - get value of current reg file
    3) Calculate what to write back based on new write data, current reg, and PPP
    Each instruction therefore takes 1 cycle for execution (2 cycles for multiply)

## Slide 6: Processor Pipeline - Stalling
Store Instruction
Branch Instruction
Multiply Instruction
Notes: Store Instruction - If store is in ID stage and instruction currently in pipeline with matching register, stall
Branch Instruction - Stall if branch reg file address is being modified in EX stage
Multiply Instruction - Stall for 32-bit multiply instruction that uses 2 cycles

## Slide 7: Processor Pipeline - Forwarding
Forward according to PPP value when:
  Write back stage destination register file = EX stage stage destination register file
  Register write is enabled in both EX and WB stages
  Applies for both R-type and Load instructions
When stalling - forward only on 1st clock cycle of stall

## Slide 8: Processor Pipeline - Branches
ID stages includes a comparator
  Determines if the register file address read is zero or not zero
The result of this ID branch signal is used to load the PC if stall if not active
If current branch in ID stage is successful, tag the instruction in IF stage to be flushed

## Slide 9: ALU
Logical Operations
  AND, OR, XOR, NOT, MOV
Arithmetic Operations
  ADD, SUB
  Multiplication
Shift Operations
  Rotate
  Logical Shift
  Arithmetic Shift
WW field determines operand widths
  Not considered for logical operations
Two-cycles for 32-bit multiplication
  One-cycle operation for all other instructions

## Slide 10: ALU - Shifters
Logical Shifting
  Left- and right-shift
  Eight 8-bit shifters
  Four 16-bit shifters
  Two 32-bit shifters
  One 64-bit shifter
Arithmetic Shifting
  Only right-shift
Shift amount - Immediate or register-value
Rotation
Coding style for arithmetic-shifting
  $signed
    Type-cast function
    Sign-extension
    Synthesizable
  “>>>”
    Verilog arithmetic right-shift operator
  result = $signed(oprA) >>> oprB[58:63];
Notes: Verilog – by default treats operands as unsigned

## Slide 11: ALU - Multipliers
8-bit Multipliers
  Four 8x8 multipliers
  Byte multiplication
16-bit Multipliers
  Two 16x16 multipliers
  Halfword multiplication
32-bit Multiplier
  Word multiplication
  One 2-stage pipelined DesignWare multiplier instance
    DW02_mult_2_stage
    Implementation - Booth-recoded Wallace-tree
Even and Odd multiplication
Square Operations
Fig. - DW02_mult_2_stage block diagram
(source - Synopsys DesignWare document library)

## Slide 12: Testing & Synthesis
Test methodology
  Write assembly code
  Perl script to convert to binary IMEM fill
  Observe waveforms and DMEM dump file
  Separate test-benches for register-file, ALU
  Test-cases
    ALU operations
    Load and Store
    Branches
    Stalling, Forwarding...
Synthesis
  Meets 4 ns clock-period requirement
  2.4 ns cycle time possible too!
  report_resources command

## Slide 13: Testing & Synthesis - contd.

## Slide 14: Q & A

## Slide 15
Instruction Formats
  R-type
  M-type
6-bits | 5-bits | 5-bits | 5-bits | 5-bits |  | 6-bits
101010 | rD | rA | rB | PPP | WW | Function_code
0 5 | 6 10 | 11 15 | 16 20 | 21 23 | 24 25 | 26 31
6-bits | 5-bits | 5-bits | 16-bits
 | rD | 00000 | Immediate_Address
0 5 | 6 10 | 11 15 | 16 31
6-bits | 5-bits | 5-bits | 5-bits | 5-bits |  | 6-bits
101010 | rD | rA | 00000 | PPP | WW | Function_code
0 5 | 6 10 | 11 15 | 16 20 | 21 23 | 24 25 | 26 31

## Slide 16
WW value | Operand Width | Assembly Mnemonic
00 | 8 | b
01 | 16 | h
10 | 32 | w
11 | 64 | d
WW | Width | Subfield indices within a 64-bit register for different operand widths |  |  |  |  |  |  |  | Data-operands
 |  | MSB |  |  |  |  |  |  | LSB | 
00 | 8 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
01 | 16 | 0 |  | 1 |  | 2 |  | 3 |  | 4
10 | 32 | 0 |  |  |  | 1 |  |  |  | 2
11 | 64 | 0 |  |  |  |  |  |  |  | 1

## Slide 17
PPP value | Participation Definition | Assembly Mnemonic
000 | All subfields participate | a
001 | Upper 32-bit participate | u
010 | Lower 32-bits participate | d
011 | Subfields with even index participate | e
100 | Subfields with odd index participate | o
101 | Reserved | None
110 | Reserved | None
111 | Reserved | None
Subfield indices within a 64-bit register for different operand widths |  |  |  |  |  |  | 
MSB |  |  |  |  |  |  | LSB
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7

## Slide 18
Sr. No. | Instruction | Format | Encoding |  |  |  |  | 
 |  |  | 6bits | 5bits | 5bits | 5bits | 5bits | 6bits
1 | VAND | R | 101010 | rD | rA | rB | PPPWW | 000001
2 | VOR | R | 101010 | rD | rA | rB | PPPWW | 000010
3 | VXOR | R | 101010 | rD | rA | rB | PPPWW | 000011
4 | VNOT | R | 101010 | rD | rA | 00000 | PPPWW | 000100
5 | VMOV | R | 101010 | rD | rA | 00000 | PPPWW | 000101
6 | VADD | R | 101010 | rD | rA | rB | PPPWW | 000110
7 | VSUB | R | 101010 | rD | rA | rB | PPPWW | 000111
8 | VMULEU | R | 101010 | rD | rA | rB | PPPWW | 001000
9 | VMULOU | R | 101010 | rD | rA | rB | PPPWW | 001001
10 | VSQEU | R | 101010 | rD | rA | 00000 | PPPWW | 001010
11 | VSQOU | R | 101010 | rD | rA | 00000 | PPPWW | 001011
12 | VRTTH | R | 101010 | rD | rA | 00000 | PPPWW | 001100
13 | VSLL | R | 101010 | rD | rA | rB | PPPWW | 001101
14 | VSLLI | R | 101010 | rD | rA | shift_amount | PPPWW | 001110
15 | VSRL | R | 101010 | rD | rA | rB | PPPWW | 001111
16 | VSRLI | R | 101010 | rD | rA | shift_amount | PPPWW | 010000
17 | VSRA | R | 101010 | rD | rA | rB | PPPWW | 010001
18 | VSRAI | R | 101010 | rD | rA | shift_amount | PPPWW | 010010
19 | VLD | M | 100000 | rD | 00000 | Immediate Address |  | 
20 | VSD | M | 100001 | rA | 00000 | Immediate Address |  | 
21 | VBEZ | R | 100010 | rD | 00000 | Immediate Address |  | 
22 | VBNEZ | R | 100011 | rD | 00000 | Immediate Address |  | 
23 | VNOP | R | 111100 | 00000 | 00000 | 00000 | 00000 | 000000